## Slide 1
Greenhouse_controller
Open Source Greenhouse Control Software
Contact: George Schreck
Email: george.schreck@gmail.com
Phone: 919-418-0542

## Slide 2: Problems
Many different greenhouse controllers on the market, but unable to identify one that meets the need of a large hobby or small commercial greenhouse and is cost effective
Commercial controllers are generally limited in function as they are designed for particular applications, i.e. temperature controllers, irrigation timers, dosing, monitoring, etc.
Commercial controllers are inflexible and not easily tailored

## Slide 3: Goals
Inexpensive, open hardware design
Open-source software that is easily modified and adapted
Modular design to enable easy customization or addition
Management of all aspects of a greenhouse:
  reporting status/errors, soil conditions, environment
  controlling: fans, swamp cooler, heat, misters, hydroponic cycles, conventional irrigation

## Slide 4: HMI
User Console for control of all aspects of operation utilizing simple command line interface
Web page reporting:
  Historical information: temperature, humidity, barometric pressure, light intensity
  Listing of all programs, if they are active and how long until their next cycle
  Report generator – csv or Excel output
Misc:
  Pause button on the controller box to turn off all Bato and conventional irrigation
  User configurable email and/or text message status, warning and error messages.

## Slide 5: Monitoring Requirements
Separate, asynchronous process spawned by “main”
Monitoring frequency software configurable
All valves checked for proper state
Temperature within user set bounds
System health:
  power out events
  Crash of environmental controller or irrigation control
  water pressure loss on NFT and main irrigation water
  Low water on irrigation tanks
  Eventually
    EC and PH
    Soil Moisture for adaptable irrigation cycles

## Slide 6: Irrigation Control Requirements
Separate, asynchronous process spawned by main
Unlimited number of simultaneous programs
Unlimited number of separate irrigation systems
Parallel operation of non-conflicting irrigation paths
On and Off time configurable by program
Number of sub-cycles and duration off and on configurable
Irrigation routing selectable by program
All requirements for pump pre-starts satisfied
Database recording of all events with user defined logging masks

## Slide 7: Environmental Control Requirements
Monitor:
  Temperature, humidity, barometric pressure and light intensity
  Control loop time configurable in software
Exhaust fan controller On and Off temperature (hysteresis) user configurable
Swamp Cooler On and Off temperature user configurable
Mister On and Off temperature user configurable
Mister cycle time configurable
Database recording of all events with user defined logging masks
Eventually
  Remote temperature sensor for outdoors, irrigation temperatures and soil temperature

## Slide 8: Main Program Requirements
Maintains all global variables
Several modes of operation:
  Initialize for new start ups – clears warm start data
  Verbose for additional operation messages
  Debug for limited run time (test mode)
All run configuration data stored in database for warm restart after power outage

## Slide 9: High Level Initial Architecture
HMI
Monitoring and Reporting
Environmental Control
Irrigation Control
Main Program
Data Logging
Console Interface
web Interface

## Slide 10: Initial Hardware
HiLetgo DHT22/AM2302 Digital Temperature and Humidity Sensor
Waveshare BME280 environmental sensor – not currently used, crashing on long runs
SHILLEHTEK GY-302 BH1750 Pre-Soldered Light Intensity I2C IIC Module for Raspberry Pi
Raspberry Pi 27W USB-C Power Supply Black US
Raspberry Pi 5/8GB SC1112
MicroSD Card - 32GB
RTC Battery for Raspberry Pi 5
EDATEC CM5 Active Cooler - ED-CM5ACOOLER
JESSINIE 16 Channel 5V Relay Module with Optocoupler Isolation 10A IIC Expandable Isolation Driver Relay Board XL9535-K16V5
3 in 1 Male to Female /Male to Male /Female to Female Breadboard Jumper Wires for Arduino and Raspberry pi